## Slide 1: Computer Organization & Design 计算机组成与设计
Weidong Wang (王维东)
wdwang@zju.edu.cn
College of Information Science & Electronic Engineering
信息与通信网络工程研究所（ICAN）
Zhejiang University

## Slide 2: Course Information
Instructor: Weidong WANG
  Email: wdwang@zju.edu.cn
  Tel(O): 0571-87953170;
  Office Hours: TBD, Yuquan Campus, Xindian (High-Tech) Building 306, /email whenever
  Mobile: 13605812196
TA:
  mobile，Email:
    孙佳科, 188-8892-3044; 22131087@zju.edu.cn;
    Office Hours: Thursday & Saturday 14:00-16:30 PM.
    Xindian (High-Tech) Building 308.（也可以短信邮件联系）

## Slide 3: Prerequisites预修课程
Logic Design
Programming
  C / JAVA / Python
  Verilog / OpenCL / C++
Compilers, OS, Circuits/VLSI background is a plus, not needed
How to learn this Course?
  Not only listening, thinking and waiting ….
  But Exercise, Simulation, Practice!

## Slide 4: Other Course Info
Course Text:
  David A. Patterson and John L. Hennessy, Computer Organization & Design: The Hardware/Software Interface, 5th edition,机械工业出版社，20142019
  “Green card” summarizes MIPS ISARISC-V
Website:
  课程教学网站：浙江大学“学在浙大” 平台
  http://mypage.zju.edu.cn/wdwd/
  Check frequently
Classroom
  玉泉教7-108 周四Thursday –六七八节

## Slide 5: Textbook Info
Textbook
  Computer Organization and Design (The HW/SW Interface) RISC-V Edition， D. Patterson & J. Hennessy, 英文版，原书第5版，RISC-V版，机械工业出版社，2019
  “Green card” summarizes RISC-V ISA

## Slide 6: Grading (Tentative)
Final grades will be computed approximately as follows:
理论课成绩100分（COD） ：
Homework Sets - 10%
  Homework Sets （10%）
Quizes - 10%
  2~4次 Quizes（随堂小测）
Two Projects and discussion - 10%
  2 projects (1 or 2 members team)
Web 网络线上学习+线上测验：30%。
Finial Exam - 40%（闭卷，英文题目，答卷中英文不限）
实验课：100分
总评最后成绩: =Lab score * (0.5/3.5) + COD * (3.0/3.5)
Notes: 上课说明此门课程的成绩合成：平时成绩包括平时小测验、期中考试、作业、出勤、课堂讨论、论文

## Slide 7: Lecture 15 Review
7

## Slide 8: Major Topics
Hardware-software interface
  Machine language and assembly language programming
Compiler optimizations and performance
Processor design
  Pipelined processor design
Memory hierarchy design
  Caches
I/O devices and systems
Virtual memory & operating systems support
Multiprocessors and Multithreading

## Slide 9: Why take this class?
Learn how modern computing hardware works
Understand where computing hardware is going in the future
  And learn how to contribute to this future…
How does this impact system software and applications?
  Essential to understand OS/compilers/PL
  For everyone else, it can help you write better code!
How are future technologies going to impact computing systems?
9
Notes: 我们许多人认为自己是搞硬件的，有人认为是搞软件的。这种说法暗示你对某一方面精通，而对另一方面知之甚少。听起来好像软件与硬件间有一堵高墙，你选择呆在墙的某一边。现在开始你要抛弃这个观念。

## Slide 10: Topics of Study
Focus on what modern computer architects worry about ( both academia and industry)
Get through the basics of modern processor design
Look at technology trends: multithreading, CMP,
power-, reliability- and security- aware design
Recent research ideas, and the future of computing hardware
10

## Slide 11: What is Computer Architecture?

## Slide 12: 5 components of any Computer
Processor
Computer
Control
(“brain”)
Datapath
(“brawn”)
Memory
(where
programs,
data
live when
running)
Devices
Input
Output
Keyboard, Mouse
Display, Printer
Disk (where
programs,
data
live when
not running)

## Slide 13: Abstraction Layers in Modern Systems
Algorithm
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Devices
Programming Language
Circuits
Physics
Original domain of the computer architect („50s-‟80s)
Domain of recent computer architecture
(„90s)
Parallel computing, security, …
Reliability, power, …
Reinvigoration of computer architecture, mid-2000s onward.

## Slide 14: Machine Structures
Parallel Requests
  Assigned to computer
  e.g., Search “Cats”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates working in parallel at same time
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Main Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s Lecture

## Slide 15: Lecture 2 Introduction to RISC-V Assembly language: Arithmetic

## Slide 16: Aside: Registers are Inside the Processor
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
Read Data
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data

## Slide 17: And in Conclusion…
In RISC-V Assembly Language:
  Registers replace C variables
  One instruction (simple operation) per line
  Simpler is Better, Smaller is Faster
In RV32, words are 32b
Instructions:
  add, addi, sub
Registers:
  32 registers, referred to as x0 – x31
  Zero: x0

## Slide 18: Big Endian vs. Little Endian
Big-endian and little-endian derive from Jonathan Swift's Gulliver's Travels《格列佛游记》 in which the Big Endians were a political faction that broke their eggs at the large end ("the primitive way") and rebelled against the Lilliputian King who required his subjects (the Little Endians) to break their eggs at the small end.
Big Endian
ADDR3 ADDR2 ADDR1 ADDR0 BYTE0 BYTE1 BYTE2 BYTE3 00000001 00000100 00000000 00000000
Examples
Names in China (e.g., Garcia Dan)
Java Packages: (e.g., org.mypackage.HelloWorld)
Dates done correctly ISO 8601 YYYY-MM-DD (e.g., 2019-08-16)
Eating Pizza crust first
Unix file structure (e.g., /usr/local/bin/python)
Little Endian
ADDR3 ADDR2 ADDR1 ADDR0 BYTE3 BYTE2 BYTE1 BYTE0 00000000 00000000 00000100 00000001
Examples
Names in the US (e.g., Dan Garcia)
Internet names (e.g., www.cs.berkeley.edu)
Dates written in England DD/MM/YYYY (e.g., 16/08/2019)
Eating Pizza skinny part first (the normal way)
Consider the number 1025 as we normally write it: BYTE3 BYTE2 BYTE1 BYTE0 00000000 00000000 00000100 00000001
The order in which BYTES are stored in memory
Bits always stored as usual. (E.g., 0xC2=0b 1100 0010)
en.wikipedia.org/wiki/Big_endian

## Slide 19: And in Conclusion…
Memory is byte-addressable, but lw and sw access one word at a time.
A pointer (used by lw and sw) is just a memory address, we can add to it or subtract from it (using offset).
A Decision allows us to decide what to execute at run-time rather than compile-time.
C Decisions are made using conditional statements within if, while, do while, for.
RISC-V Decision making instructions are the conditional branches: beq and bne.
New Instructions:
  lw, sw, lb, sb, lbu, beq, bne, blt, bltu, bge, j

## Slide 20: And in Conclusion…
Registers we know so far (Most of them!)
  a0-a7 for function arguments, a0-a1 for return values
  ra return address
  s0-s11 saved registers
  zero
Instructions we know:
  Arithmetic: add, addi, sub
  Logical: sll, srl, sla, slli, srli, slai, and, or, xor, andi, ori, xori
  Decision: beq, bne, blt, bge
  Unconditional branches (jumps): j, jr
  Functions called with jal, return with jr ra.

## Slide 21: RV32 Memory Allocation

## Slide 22: And in Conclusion…
Registers we know so far (All of them!)
  a0-a7 for function arguments, a0-a1 for return values
  sp, stack pointer, ra return address
  s0-s11 saved registers
  t0-t6 temporaries
  zero
Instructions we know:
  Arithmetic: add, addi, sub
  Logical: sll, srl, sla, slli, srli, slai, and, or, xor, andi, ori, xori
  Decision: beq, bne, blt, bge
  Unconditional branches (jumps): j, jr
  Functions called with jal, return with jr ra.
The stack is your friend: Use it to save anything you need. Just leave it the way you found it!

## Slide 23: Salient Features of MIPS I
32-bit fixed format inst (3 formats)
32 32-bit GPR (R0 contains zero) and 32 FP registers (and HI LO)
  partitioned by software convention
3-address, reg-reg arithmetic instr.
Single address mode for load/store: base+displacement
  no indirection, scaled
16-bit immediate plus LUI
Simple branch conditions
  compare against zero or two registers for =,
  no integer condition codes
Delayed branch
  execute instruction after a branch (or jump) even if the branch is taken (Compiler can fill a delayed branch with useful work about 50% of the time)

## Slide 24: R-Format Instruction Layout
32-bit instruction word divided into six fields of varying numbers of bits each: 7+5+5+3+5+7 = 32
Examples
  opcode is a 7-bit field that lives in bits 6-0 of the instruction
  rs2 is a 5-bit field that lives in bits 24-20 of the instruction
Field’s bit positions
Number of bits in field
Name of field
7
5
5
3
7
5
31
25
20
15
7
12
24
19
14
11
6
0
funct7
rs2
rs1
funct3
rd
opcode

## Slide 25: All RV32 R-format instructions
Different encoding in funct7 + funct3 selects different operations
0000000
rs2
rs1
000
rd
0110011
0100000
rs2
rs1
000
rd
0110011
0000000
rs2
rs1
001
rd
0110011
add
sub
sll
0000000
rs2
rs1
010
rd
0110011
slt
0000000
rs2
rs1
011
rd
0110011
sltu
0000000
rs2
rs1
100
rd
0110011
xor
0000000
rs2
rs1
101
rd
0110011
srl
0100000
rs2
rs1
101
rd
0110011
sra
0000000
rs2
rs1
110
rd
0110011
0000000
rs2
rs1
111
rd
0110011
or
and
Can you spot two new instructions?

## Slide 26: I-Format Instruction Layout
  Only one field is different from R-format, rs2 and funct7 replaced by 12-bit signed immediate, imm[11:0]
  Remaining fields (rs1, funct3, rd, opcode) same as before
  imm[11:0] can hold values in range [-2048ten , +2047ten ]
  Immediate is always sign-extended to 32-bits before use in an arithmetic operation
  We’ll later see how to handle immediates > 12 bits
7
5
5
3
7
5
31
25
20
15
7
12
24
19
14
11
6
0
funct7
rs2
rs1
funct3
rd
opcode
Imm[11:0]
12

## Slide 27: All RV32 I-format Arithmetic Instructions
“Shift-by-immediate” instructions only use lower 5 bits of the immediate value for shift amount (can only shift by 0-31 bit positions)
One of the higher-order immediate bits is used to distinguish “shift right logical” (SRLI) from “shift right arithmetic” (SRAI)
imm[11:0]
rs1
000
rd
0010011
imm[11:0]
rs1
010
rd
0010011
imm[11:0]
rs1
011
rd
0010011
addi
slti
sltiu
imm[11:0]
rs1
100
rd
0010011
xori
imm[11:0]
rs1
110
rd
0010011
ori
imm[11:0]
rs1
111
rd
0010011
andi
0000000
shamt
rs1
001
rd
0010011
slli
0000000
shamt
rs1
101
rd
0010011
srli
0100000
shamt
rs1
101
rd
0010011
srai

## Slide 28: All RV32 Load Instructions
LBU is “load unsigned byte”
LH is “load halfword”, which loads 16 bits (2 bytes) and sign-extends to fill destination 32-bit register
LHU is “load unsigned halfword”, which zero-extends 16 bits to fill destination 32-bit register
There is no LWU in RV32, because there is no sign/zero extension needed when copying 32 bits from a memory location into a 32-bit register
funct3 field encodes size and ‘signedness’ of load data
imm[11:0]
rs1
000
rd
0000011
imm[11:0]
rs1
010
rd
0000011
imm[11:0]
rs1
011
rd
0000011
lb
lh
lw
imm[11:0]
rs1
100
rd
0000011
lbu
imm[11:0]
rs1
110
rd
0000011
lhu

## Slide 29: S-Format Used for Stores
  Store needs to read two registers, rs1 for base memory address, and rs2 for data to be stored, as well immediate offset!
  Can’t have both rs2 and immediate in same place as other instructions!
  Note that stores don’t write a value to the register file, no rd!
  RISC-V design decision is move low 5 bits of immediate to where rd field was in other instructions – keep rs1/rs2 fields in same place
    register names more critical than immediate bits in hardware design
7
5
5
3
7
5
31
25
20
15
7
12
24
19
14
11
6
0
Imm[11:5]
rs2
rs1
funct3
imm[4:0]
opcode
offset[11:5]
base
width
src
STORE
offset[4:0]

## Slide 30: All RV32 Store Instructions
Imm[11:5]
rs2
rs1
000
imm[4:0]
0100011
sb
sh
sw
Imm[11:5]
rs2
rs1
001
imm[4:0]
0100011
Imm[11:5]
rs2
rs1
010
imm[4:0]
0100011
  Store byte, halfword, word
width

## Slide 31: RISC-V B-Format for Branches
B-format is mostly same as S-Format, with two register sources (rs1/rs2) and a 12-bit immediate imm[12:1]
But now immediate represents values -4096 to +4094 in 2-byte increments
The 12 immediate bits encode even 13-bit signed byte offsets (lowest bit of offset is always zero, so no need to store it)
1
6
5
3
7
4
31
30
24
15
7
12
25
20
14
11
6
0
imm[12]
rs2
rs1
funct3
imm[4:1]
opcode
imm[10:5]
imm[11]
19
8
5
1
BRANCH
offset[12|10:5]
rs1
funct3
rs2
offset[4:1|11]

## Slide 32: RISC-V Immediate Encoding
Instruction encodings, inst[31:0]
32-bit immediates produced, imm[31:0]
Only bit 7 of instruction changes role in immediate between S and B
Upper bits sign-extended from inst[31] always
31
25
20
15
7
12
24
19
14
11
6
0
funct7
rs2
rs1
funct3
rd
opcode
31
25
12
1
5
24
11
10
4
0
30
8
rs1
funct3
rd
opcode
imm[11:0]
imm[11:5]
rs2
rs1
funct3
imm[4:0]
opcode
R-type
I-type
S-type
imm[12|10:5]
rs2
rs1
funct3
imm[4:1|11]
opcode
B-type
inst[30:25]
inst[24:21]
inst[20]
I-imm.
-inst[31]-
inst[30:25]
inst[11:8]
inst[7]
S-imm.
-inst[31]-
inst[30:25]
inst[11:8]
0
B-imm.
-inst[31]-
inst[7]

## Slide 33: All RISC-V Branch Instructions
imm[12|10:5]
rs2
rs1
000
imm[4:1|11]
1100011
BEQ
imm[12|10:5]
rs2
rs1
001
imm[4:1|11]
1100011
BNE
imm[12|10:5]
rs2
rs1
100
imm[4:1|11]
1100011
BLT
imm[12|10:5]
rs2
rs1
101
imm[4:1|11]
1100011
BGE
imm[12|10:5]
rs2
rs1
110
imm[4:1|11]
1100011
BLTU
imm[12|10:5]
rs2
rs1
111
imm[4:1|11]
1100011
BGEU

## Slide 34: U-Format for “Upper Immediate” Instructions
Has 20-bit immediate in upper 20 bits of 32-bit instruction word
One destination register, rd
Used for two instructions
  LUI – Load Upper Immediate
  AUIPC – Add Upper Immediate to PC
7
31
7
12
6
0
opcode
imm[31:12]
rd
11
20
5
U-immediate[31:12]
dest
LUI
U-immediate[31:12]
dest
AUIPC

## Slide 35: J-Format for Jump Instructions
JAL saves PC+4 in register rd (the return address)
  Assembler “j” jump is pseudo-instruction, uses JAL but sets rd=x0 to discard return address
Set PC = PC + offset (PC-relative jump)
Target somewhere within ±219 locations, 2 bytes apart
  ±218 32-bit instructions
Immediate encoding optimized similarly to branch instruction to reduce hardware cost
7
31
7
12
6
0
opcode
imm[10:1]
rd
11
10
5
offset[20:1]
dest
JAL
imm[20]
imm[11]
imm[19:12]
1
1
8
19
20
21
30

## Slide 36: JALR Instruction (I-Format)
JALR rd, rs, immediate
  Writes PC+4 to rd (return address)
  Sets PC = rs + immediate
  Uses same immediates as arithmetic and loads
    no multiplication by 2 bytes
    In contrast to branches and JAL
7
31
7
12
6
0
opcode
imm[11:0]
rd
11
12
5
offset[11:0]
dest
JALR
rs1
func3
5
3
15
19
20
14
base
0

## Slide 37: Summary of RISC-V Instruction Formats
31
25
20
15
7
12
24
19
14
11
6
0
funct7
rs2
rs1
funct3
rd
opcode
30
8
21
rs1
funct3
rd
opcode
imm[11:0]
imm[11:5]
rs2
rs1
funct3
imm[4:0]
opcode
I-type
S-type
imm[12|10:5]
rs2
rs1
funct3
imm[4:1|11]
opcode
B-type
opcode
imm[31:12]
rd
U-type
R-type
opcode
imm[20|10:1|11]]
rd
imm[19:12]
J-type

## Slide 38: Complete RV32I ISA
Not in 2022

## Slide 39: Lecture 4 Performance, Energy & Compiler

## Slide 40: Computer Performance Metrics
Response Time (latency延迟 )
  How long does it take for my job to run?
  How long does it take to execute a job?
  How long must I wait for the database query?
Throughput吞吐量
  How many jobs can the machine run at once?
  What is the average execution rate?
  How many queries per minute?
If we upgrade a machine with a new processor what to we increase?
If we add a new machine to the lab what do we increase?

## Slide 41: Performance = Execution Time
Elapsed Time
  Counts everything (disk and memory accesses, I/O, etc.)
  A useful number, but often not good for comparison purposes
    E.g., OS & multiprogramming time make it difficult to compare CPUs
CPU time (CPU = Central Processing Unit = processor)
  Doesn’t count I/O or time spent running other programs
  Can be broken up into system time, and user time
Our focus: user CPU time
  Time spent executing the lines of code that are “in” our program
  Includes arithmetic, memory, and control instructions, …

## Slide 42: Clock Cycles
Instead of reporting execution time in seconds, we often use cycles
Clock “ticks” indicate when to start activities
Cycle time = time between ticks = seconds per cycle
Clock rate (frequency) = cycles per second (1Hz. = 1cycle/sec)
  A 2GHz clock has a 500 picoseconds (ps) cycle time.

## Slide 43: Performance and Execution Time
The program should be something real people care about
  Desktop: MS office, edit, compile
  Server: web, e-commerce, database
  Scientific: physics, weather forecasting

## Slide 44: Measuring Clock Cycles
Clock cycles/program is not an intuitive or easily determined value, so
  Clock Cycles = Instructions x Clock Cycles Per Instruction
Cycles Per Instruction (CPI) used often
CPI is an average since the number of cycles per instruction varies from instruction to instruction
  Average depends on instruction mix, latency of each inst. Type etc.
CPIs can be used to compare two implementations of the same ISA, but is not useful alone for comparing different ISAs
  An X86 add is different from a MIPS add

## Slide 45: Using CPI
Drawing on the previous equation:
To improve performance (i.e. reduce execution time)
  Increase clock rate (decrease clock cycle time) OR
  Decrease CPI OR
  Reduce the number of instructions
Designers balance cycle time against the number of cycles required
  Improving one factor may make the other one worse

## Slide 46: Speedup
Speedup allows us to compare different CPUs or optimizations
Example
  Original CPU takes 2 seconds to run a program
  New CPU takes 1.5 seconds to run a program
  Speedup = 1.333 or speedup or 33%

## Slide 47: Amdahl’s Law
If an optimization improves a fraction f of execution time by a factor of a
This formula is known as Amdahl’s Law
Lessons from
  If f->100%, then speedup = a
  If a->∞, the speedup = 1/(1-f)
Summary
  Make the common case fast
  Watch out for the non-optimized component

## Slide 48: Procedure Call and Return
Procedures are required for structured programming
  Aka: functions, methods, subroutines, …
Implementing procedures in assembly requires several things to be done
  Memory space must be set aside for local variables
  Arguments must be passed in and return values passed out
  Execution must continue after the call
Procedure Call Steps
  1. Place parameters in a place where the procedure can access them
  2. Transfer control to the procedure
  3. Acquire the storage resources needed for the procedure
  4. Perform the desired task
  5. Place the result value in a place where the calling program can access it
  6. Return control to the point of origin

## Slide 49: Call and Return
To jump to a procedure, use the jal or jalr instructions
jal target # Jump and link to label
jalr $dest # Jump and link to $dest
Jump and link
  The program counter (PC) stores the address of the currently executing instruction
  The “jump and link” instructions stores the next instruction address in $ra before transferring control to the target/destination
  Therefore, the address stored in $ra is PC + 4
To return, use the jr instruction
jr $ra

## Slide 50: Lecture 5 RISC-V Datapath

## Slide 51: One-Instruction-Per-Cycle RISC-V Machine
On every tick of the clock, the computer executes one instruction
Current state outputs drive the inputs to the combinational logic, whose outputs settles at the values of the state before the next clock edge
At the rising clock edge, all the state elements are updated with the combinational logic outputs, and execution moves to the next clock cycle
Reg[]
pc
IMEM
DMEM
Combinational Logic
clock

## Slide 52: Basic Phases of Instruction Execution
IMEM
+4
rs2
rs1
rd
Reg[ ]
ALU
DMEM
imm
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Register
Write
PC
mux
Clock
time

## Slide 53: Recap: Complete RV32I ISA
RV32I has 47 instructions
37 instructions are enough to run any C program
Not in 2022

## Slide 54: Complete RV32I Datapath!
+4
Add
addr
inst
IMEM
pc+4
pc+4
wb
pc
wb
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn
ALUSel
Asel
MemRW
0
1
Imm[31:0]
Imm.
Gen
Add
clk
addr
inst
IMEM
DMEM
addr
DataR
DataW
PC
Inst [31:7]
1
0
2
clk
WBSel
Branch
Comp
1
0
ImmSel
1
0
PCSel
BrUn
BrEq
BrLT
Control logic
Bsel
mem
alu
alu

## Slide 55: Recap
We have designed a complete datapath
  Capable of executing all RISC-V instructions in one cycle each
  Not all units (hardware) used by all instructions
5 Phases of execution
  IF, ID, EX, MEM, WB
  Not all instructions are active in all phases
Controller specifies how to execute instructions
  New instructions can be added with just control?

## Slide 56: Lecture 6 RISC-V Control

## Slide 57: Single-Cycle RV32I Datapath and Control
+4
Add
addr
inst
IMEM
pc+4
pc+4
wb
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn
ALUSel
Asel
MemRW
0
1
Imm[31:0]
Imm.
Gen
Add
clk
addr
inst
IMEM
DMEM
addr
DataR
DataW
PC
Inst [31:20]
1
0
2
clk
WBSel
Branch
Comp
1
0
ImmSel
1
0
PCSel
BrUn
BrEq
BrLT
Bsel
Control logic
mem

## Slide 58: ROM-based Control
ROM
Inst[30,14:12,6:2]
BrEq
9
PCSel
ALUSel[3:0]
4
11-bit address (inputs)
15 data bits (outputs)
BrLT
ImmSel[2:0]
3
BrUn
ASel
BSel
MemRW
RegWEn
WBSel[1:0]
2

## Slide 59: ROM Controller Implementation
Control Word for add
Control Word for sub
Control Word for or
.
.
.
Address
Decoder
.
.
.
Inst[]
BrEQ
BrLT
Controller output (PCSel, ImmSel, …)
add
sub
or
jal
11
AND
OR

## Slide 60: Lecture 7 RISC-V Pipeline

## Slide 61: Pipelining Lessons (1/2)
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Multiple tasks operating simultaneously using different resources
Potential speedup = Number pipe stages
Time to “fill” pipeline and time to “drain” it reduces speedup: 2.3X v. 4X in this example
6 PM
7
8
9
Time
30
30
30
30
30
30
30
T
a
s
k
O
r
d
e
r
B
C
D
A

## Slide 62: Pipelining with RISC-V
Phase | Pictogram | tstep Serial
Instruction Fetch |  | 200 ps
Reg Read |  | 100 ps
ALU |  | 200 ps
Memory |  | 200 ps
Register Write |  | 100 ps
tinstruction |  | 800 ps
add t0, t1, t2
or t3, t4, t5
sll t6, t0, t3
tcycle
instruction sequence
tinstruction
tcycle Pipelined
200 ps
200 ps
200 ps
200 ps
200 ps
1000 ps
Notes: Tc = “Time between completion of instructions”

## Slide 63: Sequential vs Simultaneous
add t0, t1, t2
or t3, t4, t5
sll t6, t0, t3
tcycle
= 200 ps
instruction sequence
tinstruction = 1000 ps
sw t0, 4(t3)
lw t0, 8(t3)
addi t2, t2, 1
What happens sequentially, what happens simultaneously?
Notes: Tc = “Time between completion of instructions”

## Slide 64: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)
lw t0, 8(t3)
Pipeline registers separate stages, hold data for each instruction in flight

## Slide 65: Pipelining Hazards
A hazard is a situation that prevents starting the next instruction in the next clock cycle
Structural hazard
  A required resource is busy (e.g. needed in multiple stages)
Data hazard
  Data dependency between instructions
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Flow of execution depends on previous instruction

## Slide 66: Structural Hazard: Memory Access
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
instruction sequence
sw t0, 4(t3)
lw t0, 8(t3)
Instruction and data memory used simultaneously
  Use two separate memories

## Slide 67: Structural Hazards – Summary
Conflict for use of a resource
In RISC-V pipeline with a single memory
  Load/store requires data access
  Without separate memories, instruction fetch would have to stall for that cycle
    All other operations in pipeline would have to wait
Pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches
RISC ISAs (including RISC-V) designed to avoid structural hazards
  e.g. at most one memory access/instruction

## Slide 68: Data Hazard: ALU Result
add s0, t0, t1
sub t2, s0, t0
or t6, s0, t3
instruction sequence
xor t5, t1, s0
sw s0, 8(t3)
5 | 5 | 5 | 5 | 5/9 | 9 | 9 | 9 | 9
Value of s0
Without some fix, sub and or will calculate wrong result!

## Slide 69: Solution 1: Stalling小隔间
Problem: Instruction depends on result from previous instruction
  add s0, t0, t1 sub t2, s0, t3
Bubble气泡:
  effectively NOP: affected pipeline stages do “nothing”

## Slide 70: Solution 2: Forwarding转发
add t0, t1, t2
or t3, t0, t5
sub t6, t0, t3
instruction sequence
xor t5, t1, t0
sw t0, 8(t3)
5 | 5 | 5 | 5 | 5/9 | 9 | 9 | 9 | 9
Value of t0
Forwarding: grab operand from pipeline stage,
rather than register file

## Slide 71: Forwarding Path
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
Forwarding Control Logic

## Slide 72: Control Hazards
beq t0, t1, label
sub t2, s0, t5
or t6, s0, t3
xor t5, t1, s0
sw s0, 8(t3)
executed regardless of branch outcome!结果
executed regardless of branch outcome!!!
PC updated reflecting branch outcome

## Slide 73: Increasing Processor Performance
Clock rate
  Limited by technology and power dissipation
Pipelining
  “Overlap” instruction execution
  Deeper pipeline: 5 => 10 => 15 stages
    Less work per stage  shorter clock cycle
    But more potential for hazards (CPI > 1)
Multi-issue “superscalar” processor

## Slide 74: Lecture 8 Floating Point

## Slide 75: Floating Point Representation (1/2)
Normal format: +1.xxx…xtwo*2yyy…ytwo
Multiple of Word Size (32 bits)
0
31
S
Exponent
30
23
22
Significand
1 bit
8 bits
23 bits
S represents Sign Exponent represents y’s Significand represents x’s
Represent numbers as small as 2.0 x 10-38 to as large as 2.0 x 1038

## Slide 76: IEEE 754 Floating Point Standard (1/3)
Single Precision (DP similar):
Sign bit:1 means negative, 0 means positive
Significand:
  To pack more bits, leading 1 implicit for normalized numbers
  1 + 23 bits single, 1 + 52 bits double
  always true: 0 < Significand < 1 (for normalized numbers)
Note: 0 has no leading 1, so reserve exponent value 0 just for number 0
0
31
S
Exponent
30
23
22
Significand
1 bit
8 bits
23 bits

## Slide 77: IEEE 754 Floating Point Standard (3/3)
Called Biased Notation, where bias is number subtracted to get real number
  IEEE 754 uses bias of 127 for single prec.
  Subtract 127 from Exponent field to get actual value for exponent
  1023 is bias for double precision
Summary (single precision, or fp32):
0
31
S
Exponent
30
23
22
Significand
1 bit
8 bits
23 bits
(-1)S x (1 + Significand) x 2(Exponent-127)
  Double precision identical, except with exponent bias of 1023 (half, quad similar)

## Slide 78: Representation for ± ∞
In FP, divide by 0 should produce ± ∞, not overflow.
Why?
  OK to do further computations with ∞ E.g., X/0 > Y may be a valid comparison
  Ask math majors
IEEE 754 represents ± ∞
  Most positive exponent指数reserved for ∞
  Significands尾数all zeroes

## Slide 79: Special Numbers
What have we defined so far? (Single Precision)
  Exponent Significand Object
  0 0 0
  0 nonzero ???
  1-254 anything +/- fl. pt. #
  255 0 +/- ∞
  255 nonzero ???

## Slide 80: Conclusion
Floating Point lets us:
  Represent numbers containing both integer and fractional parts; makes efficient use of available bits.
  Store approximate values for very large and very small #s.
IEEE 754 Floating Point Standard is most widely accepted attempt to standardize interpretation of such numbers (Every desktop or server computer sold since ~1997 follows these conventions)
Summary (single precision):
0
31
S
Exponent
30
23
22
Significand
1 bit
8 bits
23 bits
(-1)S x (1 + Significand) x 2(Exponent-127)
  Double precision identical, except with exponent bias of 1023 (half, quad similar)
Exponent tells Significand how much (2i) to count by (…, 1/4, 1/2, 1, 2, …)
Can store NaN, ± ∞

## Slide 81: Lecture 9 Memory System: Cache

## Slide 82: Real Memory Reference Patterns
Donald J. Hatfield, Jeanette Gerald: Program Restructuring for Virtual Memory. IBM Systems Journal 10(3): 168-192 (1971)
Time
Memory Address (one dot per access)

## Slide 83: Memory Reference Patterns
Donald J. Hatfield, Jeanette Gerald: Program Restructuring for Virtual Memory. IBM Systems Journal 10(3): 168-192 (1971)
Time
Memory Address (one dot per access)
Spatial
Locality
Temporal
Locality

## Slide 84: Two predictable properties of memory references:局部性
Temporal Locality: If a location is referenced it is likely to be referenced again in the near future.
Spatial Locality: If a location is referenced it is likely that locations near it will be referenced in the near future.

## Slide 85: What to Do About Locality局部性
Temporal Locality
  If a memory location is referenced then it will tend to be referenced again soon
   Keep most recently accessed data items closer to the processor
Spatial Locality
  If a memory location is referenced, the locations with nearby addresses will tend to be referenced soon
   Move blocks consisting of contiguous words closer to the processor
Notes: How does the memory hierarchy work? Well it is rather simple, at least in principle.
In order to take advantage of the temporal locality, that is the locality in time, the memory hierarchy will keep those more recently accessed data items closer to the processor because chances are (points to the principle), the processor will access them again soon.
In order to take advantage of the spatial locality, not ONLY do we move the item that has just been accessed to the upper level, but we ALSO move the data items that are adjacent to it.

## Slide 86: Cache in a Computer
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
ReadData
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data
Cache
Processor organized around words and bytes
Memory (including
cache) organized around blocks, which are typically multiple words

## Slide 87: Direct-Mapped Cache (1/4)
In a direct-mapped cache, each memory address is associated with one possible block within the cache
  Therefore, we only need to look in a single location in the cache for the data if it exists in the cache
  Block is the unit of transfer between cache and memory

## Slide 88: One More Detail: Valid Bit
When start a new program, cache does not have valid information for this program
Need an indicator whether this tag entry is valid for this program
Add a “valid bit” to the cache tag entry
  0 => cache miss, even if by chance, address = tag
  1 => cache hit, if processor address = tag

## Slide 89: Multiword-Block Direct-Mapped Cache
Four words/block, cache size = 4K words
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 15 14 13 . . . 4 3 2 1 0
Byte offset
18
18
Tag
Hit
AND
“MUX” 41 Multiplexor
Data
32
Block offset
2
What kind of locality are we taking advantage of?
Notes: to take advantage for spatial locality want a cache block that is larger than word word in size.

## Slide 90: Types of Cache Misses (1/2)
“Three Cs” Model of Misses
1st C: Compulsory强制的Misses
  occur when a program is first started
  cache does not contain any of that program’s data yet, so misses are bound to occur
  can’t be avoided easily, so won’t focus on these in this course
  Every block of memory will have one compulsory miss (NOT only every block of the cache)

## Slide 91: Types of Cache Misses (2/2)
2nd C: Conflict Misses
  miss that occurs because two distinct memory addresses map to the same cache location
  two blocks (which happen to map to the same location) can keep overwriting each other
  big problem in direct-mapped caches
  how do we lessen the effect of these?
Dealing with Conflict Misses
  Solution 1: Make the cache size bigger
    Fails at some point
  Solution 2: Multiple distinct blocks can fit in the same cache Index?

## Slide 92: Fully Associative Cache (1/3)
Memory address fields:
  Tag: same as before
  Offset: same as before
  Index: non-existant
What does this mean?
  no “rows”: any block can go anywhere in the cache
  must compare with all tags in entire cache to see if data is there

## Slide 93: Fully Associative Cache (2/3)
Fully Associative Cache (e.g., 32 B block)
  compare tags in parallel
Byte Offset
:
Cache Data
B 0
0
4
31
:
Cache Tag (27 bits long)
Valid
:
B 1
B 31
:
Cache Tag
=
=
=
=
=
:

## Slide 94: Final Type of Cache Miss
3rd C: Capacity Misses
  miss that occurs because the cache has a limited size
  miss that would not occur if we increase the size of the cache
  sketchy definition, so just get the general idea
This is the primary type of miss for Fully Associative caches.

## Slide 95: N-Way Set Associative关联Cache (1/3)
Memory address fields:
  Tag: same as before
  Offset: same as before
  Index: points us to the correct “row” (called a set in this case)
So what’s the difference?
  each set contains multiple blocks
  once we’ve found correct set, must compare with all tags in that set to find our data
  Size of $ is # of sets x N blocks x block size

## Slide 96: 4-Way Set Associative Cache Circuit
tag
index
“One Hot” Encoding

## Slide 97: Block Replacement Policy
Direct-Mapped Cache
  index completely specifies position which position a block can go in on a miss
N-Way Set Assoc
  index specifies a set, but block can occupy any position within the set on a miss
Fully Associative
  block can be written into any position
Question: if we have the choice, where should we write an incoming block?
  If there’s a valid bit off, write new block into first invalid.
  If all are valid, pick a replacement policy
    rule for which block gets “cached out” on a miss.

## Slide 98: Block Replacement Policy
LRU (Least Recently Used)最近最少使用
  Idea: cache out block which has been accessed (read or write) least recently
  Pro: temporal locality  recent past use implies likely future use: in fact, this is a very effective policy
  Con: with 2-way set assoc, easy to keep track (one LRU bit); with 4-way or greater, requires complicated hardware and much time to keep track of this
FIFO
  Idea: ignores accesses, just tracks initial order
Random
  If low temporal locality of workload, works ok

## Slide 99: Improving Miss Penalty
When caches first became popular, Miss Penalty ~ 10 processor clock cycles
Today 2.4 GHz Processor (0.4 ns per clock cycle) and 80 ns to go to DRAM  200 processor clock cycles!
Proc
$2
DRAM
$
MEM
Solution: another cache between memory and the processor cache: Second Level (L2) Cache

## Slide 100: Analyzing Multi-level cache hierarchy
Proc
$2
DRAM
$
L1 hit
time
L1 Miss Rate
L1 Miss Penalty
Avg Mem Access Time =
L1 Hit Time + L1 Miss Rate * L1 Miss Penalty
L1 Miss Penalty =
L2 Hit Time + L2 Miss Rate * L2 Miss Penalty
Avg Mem Access Time =
L1 Hit Time + L1 Miss Rate * (L2 Hit Time + L2 Miss Rate * L2 Miss Penalty)
L2 hit
time
L2 Miss Rate
L2 Miss Penalty

## Slide 101: Example: with L2 cache
Assume
  L1 Hit Time = 1 cycle
  L1 Miss rate = 5%
  L2 Hit Time = 5 cycles
  L2 Miss rate = 15% (% L1 misses that miss)
  L2 Miss Penalty = 200 cycles
L1 miss penalty = 5 + 0.15 * 200 = 35
Avg mem access time = 1 + 0.05 x 35 = 2.75 cycles

## Slide 102: Kilo, Mega, Giga, Tera, Peta, Exa, Zetta, Yotta
Common use prefixes (all SI, except K [= k in SI])
Confusing! Common usage of “kilobyte” means 1024 bytes, but the “correct” SI value is 1000 bytes
Hard Disk manufacturers & Telecommunications are the only computing groups that use SI factors
  What is advertised as a 1 TB drive actually holds about 90% of what you expect
  A 1 Mbit/s connection transfers 106 bps.
Name | Abbr | Factor | SI size
Kilo | K | 210 = 1,024 | 103 = 1,000
Mega | M | 220 = 1,048,576 | 106 = 1,000,000
Giga | G | 230 = 1,073,741,824 | 109 = 1,000,000,000
Tera | T | 240 = 1,099,511,627,776 | 1012 = 1,000,000,000,000
Peta | P | 250 = 1,125,899,906,842,624 | 1015 = 1,000,000,000,000,000
Exa | E | 260 = 1,152,921,504,606,846,976 | 1018 = 1,000,000,000,000,000,000
Zetta | Z | 270 = 1,180,591,620,717,411,303,424 | 1021 = 1,000,000,000,000,000,000,000
Yotta | Y | 280 = 1,208,925,819,614,629,174,706,176 | 1024 = 1,000,000,000,000,000,000,000,000

## Slide 103: Recap
We’ve discussed memory caching in detail. Caching in general shows up over and over in computer systems
  Filesystem cache, Web page cache, Game databases / tablebases, Software memoization, Others?
Big idea: if something is expensive but we want to do it repeatedly, do it once and cache the result.
Cache design choices:
  Size of cache: speed v. capacity
  Block size (i.e., cache aspect ratio)
  Write Policy (Write through v. write back
  Associativity choice of N (direct-mapped v. set v. fully associative)
  Block replacement policy
  2nd level cache?
  3rd level cache?
Use performance model to pick between choices, depending on programs, technology, budget, ...

## Slide 104
Cache

## Slide 105: Cache Terminology
Block – Minimum unit of information transfer between levels of the hierarchy
  Block addressing varies by technology at each level
  Blocks are moved one level at a time
Hit – Data appears in a block in lower numbered level
Hit rate – Percent of accesses found
Hit time – Time to access at lower nuumbered level
  Hit time = Cache access time + Time to determine hit/miss
Miss – Data was not in lower numbered level and had to be fetched from a higher numbered level
Miss rate – Percent of misses (1 – Hit rate)
Miss penalty – Overhead in getting data from a higher numbered level
  Miss penalty = higher level access time + Time to deliver to lower level + Cache replacement/forward to processor time
  Miss penalty is usually much larger than the hit time

## Slide 106: Associative Cache Example

## Slide 107: A Typical Memory Hierarchy
L1 Data Cache
L1
Instruction Cache
Unified L2 Cache
RF
Memory
Memory
Memory
Memory
Multiported register file (part of CPU)
Split instruction & data primary caches
(on-chip SRAM)
Multiple interleaved memory banks
(off-chip DRAM)
Large unified secondary cache (on-chip SRAM)
CPU
Notes: Implementation close to the CPU looks like a Harvard machine.

## Slide 108: Direct-Mapped Cache
Tag
Data Block
V
=
Block
Offset
Tag
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines

## Slide 109: 2-Way Set-Associative Cache
Tag
Data Block
V
=
Block
Offset
Tag
Index
t
k
b
HIT
Tag
Data Block
V
Data
Word
or Byte
=
t
Notes: Compare latency to direct mapped case?

## Slide 110: Fully Associative Cache
Tag
Data Block
V
=
Block
Offset
Tag
t
b
HIT
Data
Word
or Byte
=
=
t

## Slide 111: Causes for Cache Misses
Compulsory: first-reference to a block a.k.a. cold start misses
- misses that would occur even with infinite cache
Capacity: cache is too small to hold all data needed by the program
- misses that would occur even under perfect
replacement policy
Conflict: misses that occur because of collisions
due to block-placement strategy
    misses that would not occur with full associativity
Coherence

## Slide 112
Lecture 10
Virtual Memory

## Slide 113: Bare Machine原始机
In a bare machine, the only kind of address is a physical address, corresponding to address lines of actual hardware memory.
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Physical Address

## Slide 114: Dynamic Address Translation
Motivation
  In early machines, I/O was slow and each I/O transfer involved the CPU (programmed I/O)
  Higher throughput possible if CPU and I/O of 2 or more programs were overlapped, how?
  → multiprogramming with DMA I/O devices, interrupts
Location-independent programs
  Programming and storage management ease
  → need for a base register
Protection
  Independent programs should not affect each other inadvertently
  → need for a bound register
Multiprogramming drives requirement for resident supervisor software to manage context switches between multiple programs
Physical Memory
Program 1
Program 2
OS

## Slide 115: Motivation #1: Large Address Space for Each Executing Program
Each program thinks it has a ~232 byte address space of its own
  May not use it all though
Available main memory may be much smaller

## Slide 116: Simple Base and Bound Translation
Load X
Program Address Space
Bound
Register
Bounds
Violation?
Physical Memory
Current
Segment
Base
Register
+
Physical
Address
Logical
Address
Base and bounds registers are visible/accessible only when processor is running in the supervisor mode
Base Physical Address
Segment Length
≥

## Slide 117: Separate Areas for Program and Data
Physical Address
Physical Address
Load X
Program Address Space
Physical Memory
Data Segment
Data Bound Register
Data Base Register
+
Bounds Violation?
Program Bound Register
Program Base Register
+
Program Segment
Logical Address
Logical Address
What is an advantage of this separation?
What about more base/bound pairs?
(Scheme used on all Cray vector supercomputers prior to X1, 2002)
≥
≥
Bounds Violation?
Program Counter
Notes: Permits sharing of program segments.

## Slide 118: Base and Bound约束Machine
Can fold addition of base register into (register+immediate) address calculation using a carry-save adder (sums three numbers with only a few gate delays more than adding two numbers)
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Data Bound Register
Data Base Register
+
Logical Address
Bounds Violation?
Physical Address
Program Base Register
+
Logical Address
Bounds Violation?
≥
≥
Program Bound Register

## Slide 119: Paged Memory Systems
Program-generated (virtual or logical) address split into:
Virtual Address Space Pages for Job 1
Page Table
for Job 1
Page Table contains physical address of start of each fixed-sized page in virtual address space
Physical Memory
Pages
Page Number
Offset
0
1
2
3
0
1
2
3
1
0
3
2
Paging makes it possible to store a large contiguous virtual memory space using non-contiguous physical memory pages
Notes: Relaxes the contiguous allocation requirement.

## Slide 120: Private Address Space per User
Virtual Address Space Pages for Job 1
Page Table
for Job 1
Physical Memory
Pages
0
1
2
3
0
1
2
3
1
0
1
3
3
3
2
0
0
2
2
1
Operating
System
Pages
Virtual Address Space Pages for Job 2
Page Table
for Job 2
0
1
2
3
0
1
2
3
Virtual Address Space Pages for Job 3
Page Table
for Job 3
0
1
2
3
0
1
2
3
Notes: Relaxes the contiguous allocation requirement.

## Slide 121: Page Tables Live in Memory
Virtual Address Space Pages for Job 1
Physical Memory
Pages
0
1
2
3
Page Table
for Job 1
1
0
1
3
3
2
0
2
Virtual Address Space Pages for Job 2
0
1
2
3
Page Table
for Job 2
Simple linear page tables are too large, so hierarchical page tables are commonly used (see later)
Common for modern OS to place page tables in kernel’s virtual memory (page tables can be swapped to secondary storage)
Notes: Relaxes the contiguous allocation requirement.

## Slide 122: What Does the OS do?
OS is the (first) thing that runs when computer starts
Finds and controls all devices in the machine in a general way
  Relying on hardware specific “device drivers”
Starts services (100+)
  File system,
  Network stack (Ethernet, WiFi, Bluetooth, …),
  TTY (keyboard),
  …
Loads, runs and manages programs:
  Multiple programs at the same time (time-sharing)
  Isolate programs from each other (isolation)
  Multiplex resources between applications (e.g., devices)

## Slide 123: Supervisor Mode监管者模式
If something goes wrong in an application, it could crash the entire machine. And what about malware恶意代码, etc.?
The OS enforces resource constraints to applications (e.g., access to memory, devices)
To help protect the OS from the application, CPUs have a supervisor mode (e.g., set by a status bit in a special register)
  A process can only access a subset of instructions and (physical) memory when not in supervisor mode (user mode)
  Process can change out of supervisor mode using a special instruction, but not into it directly – only using an interrupt
  Supervisory mode is a bit like “superuser”
    But used much more sparingly (most of OS code does not run in supervisory mode)
    Errors in supervisory mode often catastrophic (blue “screen of death”, or “I just corrupted your disk”)

## Slide 124: Syscalls
What if we want to call an OS routine? E.g.,
  to read a file,
  launch a new process,
  ask for more memory (malloc),
  send data, etc.
Need to perform a syscall:
  Set up function arguments in registers,
  Raise software interrupt (with special assembly instruction)
OS will perform the operation and return to user mode
This way, the OS can mediate access to all resources, and devices

## Slide 125: Multiprogramming
The OS runs multiple applications at the same time
But not really (unless you have a core per process)
Switches between processes very quickly (on human time scale) – this is called a “context switch”
When jumping into process, set timer (we will call this ‘interrupt’)
  When it expires, store PC, registers, etc. (process state)
  Pick a different process to run and load its state
  Set timer, change to user mode, jump to the new PC
Deciding what process to run is called scheduling

## Slide 126: Protection, Translation, Paging
Supervisor mode alone is not sufficient to fully isolate applications from each other or from the OS
  Application could overwrite another application’s memory.
  Typically programs start at some fixed address, e.g. 0x8FFFFFFF
    How can 100’s of programs share memory at location 0x8FFFFFFF?
  Also, may want to address more memory than we actually have (e.g., for sparse data structures)
Solution: Virtual Memory
  Gives each process the illusion of a full memory address space that it has completely for itself

## Slide 127: Virtual vs. Physical Addresses
Processes use virtual addresses, e.g., 0 … 0xffff,ffff
  Many processes, all using same (conflicting) addresses
Memory uses physical addresses (also, e.g., 0 ... 0xffff,ffff)
Memory manager maps virtual to physical addresses
Processor (& Caches)
Control
Datapath
PC
Registers
(ALU)
Memory (DRAM)
Bytes
?
Virtual Address
Physical Address
Many of these (software & hardware cores)
One main memory

## Slide 128: Paged Memory
Page N
Page 2
Page 1
Page 0
Memory (DRAM)
Page Table
Page Table
Page Table
Each process has a dedicated page table. Physical memory non-consecutive.

## Slide 129: Paged Memory Address Translation
OS keeps track of which process is active
  Chooses correct page table
Memory manager extracts page number from virtual address
  e.g. just top 20 bits
Looks up page address in page table
Computes physical memory address from sum of
  Page address and
  Offset (from virtual address)
page table entry | offset
Virtual address (e.g. 32 Bits)
page number | offset
Physical address
Physical addresses may (but do not have to) have more or fewer bits than virtual addresses

## Slide 130: Paged Table Storage in DRAM
Page Table
Page Table
Page
Page Table
Memory (DRAM)
lw/sw take two memory references

## Slide 131: Memory Access
Check page table entry:
  Valid?
    Yes, valid  In DRAM?
      Yes, in DRAM: read/write data
      No, on disk: allocate new page in DRAM
        If out of memory, evict a page from DRAM
        Store evicted page to disk
        Read page from disk into memory
        Read/write data
    Not Valid
      allocate new page in DRAM
        If out of memory, evict a page
        Read/write data
Page fault
OS intervention

## Slide 132: Hierarchical Page Table
Level 1
Page Table
Page size 10b  1024 x 4096B
Level 2
Page Tables
12b  4096B
Data Pages
page in primary memory (DRAM)
page in secondary memory (disk)
Root of the Current
Page Table
p1
p2
Virtual Address
(Processor Register)
PTE of a nonexistent page
p1 p2 offset
0
11
12
21
22
31
10-bit
L1 index
10-bit
L2 index
Physical Memory
Exploits Sparsity of Virtual Address Space Use
Supervisor page table base register (SPTBR) in RISC-V

## Slide 133: Translation Lookaside Buffers (TLB转换快表)
Address translation is very expensive!
  In a single-level page table, each reference becomes two memory accesses
  In a two-level page table, each reference becomes three memory accesses
Solution: Cache some translations in TLB
TLB hit  Single-Cycle Translation
TLB miss  Page-Table Walk to refill
VPN offset
V D tag PPN
physical address
PPN offset
virtual address
hit?
(VPN = virtual page number)
(PPN = physical page number)
Notes: 3 memory references
V – valid
R – referenced (know what to evict from cache)
R –
D – dirty (page was written to)

## Slide 134: Where Are TLBs Located?
Which should we check first: Cache or TLB?
  Can cache hold requested data if corresponding page is not in physical memory?
  With TLB first, does cache receive VA or PA?
No
PA
Cache
VA
PA
miss
hit
data
hit
miss
CPU
Main Memory
TLB
Page Table
Notice that it is now the TLB that does translation, not the Page Table!

## Slide 135: Address Translation Using TLB
TLB Tag
TLB Index
Page Offset
TLB Tag | PPN
(used just like in a cache) | 
. . . | 
TLB
VPN
PPN
Page Offset
Tag
Index
Offset
Virtual Address
Physical Address
 | Tag | Block Data
. . . |  | 
Data Cache
PA split two different ways!
Note: TIO for VA & PA unrelated

## Slide 136: VM-related Events in Pipeline
Handling a TLB miss needs a hardware or software mechanism to refill TLB
  Usually done in hardware
Protection violation may abort process
PC
Inst TLB
Inst. Cache
D
Decode
E
M
Data TLB
Data Cache
W
+
TLB miss? Page Fault?
Protection violation?
TLB miss? Page Fault?
Protection violation?

## Slide 137: Page-Based Virtual-Memory Machine (Hardware Page-Table Walk)
Assumes page tables held in untranslated physical memory
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Page Fault?
Protection violation?
Page Fault?
Protection violation?
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Physical Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?

## Slide 138: Address Translation: putting it all together
Virtual Address
TLB
Lookup
Page Table
Walk
Update TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
(to cache)
miss
hit
the page is
Ï memory Î memory
denied
permitted
Protection
Fault
hardware
hardware or software
software
SEGFAULT
Where?
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 139: Impact of Paging on AMAT (1/2)
Memory Parameters:
  L1 cache hit = 1 clock cycles, hit 95% of accesses
  L2 cache hit = 10 clock cycles, hit 60% of L1 misses
  DRAM = 200 clock cycles (≈100 nanoseconds)
  Disk = 20,000,000 clock cycles (≈10 milliseconds)
Average Memory Access Time (no paging):
  1 + 5%×10 + 5%×40%×200 = 5.5 clock cycles
Average Memory Access Time (with paging):
  5.5 (AMAT with no paging) + ?

## Slide 140: Memory Mapped I/O
Certain addresses are not regular memory
Instead, they correspond to registers in I/O devices
ctrl reg.
data reg.
0xFFFFFFFF
0x00000000
0x8000000
address
0x7FFFFFFF
Memory-mapped
Program & Data Memory

## Slide 141: Review: Typical x86 PC I/O System

## Slide 142: Increasing Bus Bandwidth

## Slide 143: Communication with the CPU
Method #1: Polling轮询
  I/O device places information in a status register
  The OS periodically checks the status register
  Whether polling is used dependent upon whether the device can initiate I/O independently
    For instance, a mouse works well since it has a fixed I/O rate and initiates its own data (whenever it is moved)
    For others, such as disk access, I/O only occurs under the control of the OS, so we poll only when the OS knows it is active
  Advantages
    Simple to implement
    Processor is in control and does the work
  Disadvantage
    Polling overhead and data transfer consume CPU time

## Slide 144: I/O Interrupts
中断向量
中断服务程序

## Slide 145: Delegating授权委派I/O: DMA
Direct Memory Access (DMA)
  Transfer blocks of data to or from memory without CPU intervention
  Communication coordinated by the DMA controller
    DMA controllers are integrated in memory or I/O controller chips
  DMA controller acts as a bus master, in bus-based systems
DMA steps
  Processor sets up DMA by supplying
    Identify识别确定of the device and the operation (read/write)
    The memory address for source/destination
    The number of bytes to transfer
  DMA controller starts the operation by arbitrating仲裁for the bus and then starting the transfer when the data is ready
  Notify the processor when the DMA transfer is complete or on error
    Usually using an interrupt

## Slide 146: DMA & Coherence一致性
Solution 1: OS flushes冲刷the cache before I/O reads or forces write backs before I/O writes
  Flush/write-back may involve selective addresses or whole cache
  Can be done in software or with hardware (ISA) support
Solution 2: Route memory accesses for I/O through the cache
  Search the cache for copies and invalidate or write-back as needed
  This hardware solution may impact performance negatively消极地
    While searching cache for I/O requests, it is not available to processor
  Multi-level, inclusive包容性caches make this easier
    Processor searches L1 cache mostly (until it misses)
    I/O requests search L2 cache mostly *until it finds a copy of interest)

## Slide 147: I/O Summary
I/O performance has to take into account many variables
  Response time and throughput
  CPU, memory, bus, I/O device
  Workload e.g. transaction processing
I/O devices also span a wide spectrum
  Disks, graphics, and networks
Buses
  Bandwidth
  Synchronization
  Transactions
OS and I/O
  Communication: Polling轮询and Interrupts
  Handling I/O outside CPU: DMA

## Slide 148: Lecture 11 Hardware Architectural Support for Operating System
148

## Slide 149: Page-Based Virtual-Memory Machine (Hardware Page-Table Walk)
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Page Fault?
Protection violation?
Page Fault?
Protection violation?
Assumes page tables held in untranslated physical memory
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Physical Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?
Notes: CS252 S05
149

## Slide 150: Processes进程
Definition: a process is an instance实例 of a running program
Process provides each program with two key abstractions
  Logical control flow
    Illusion of exclusive use of the processor
    Private set of register values (including PC)
  Private address space
    Illusion of exclusive use of main memory of “infinite” size
How are these illusion错觉maintained?
  Process execution is interleaved分时交错 (multitasking)
    On available processors
  Address space is managed by virtual memory system
150
专用的错觉

## Slide 151: Supporting Concurrent Processes through Context Switching上下文切换
151
1
2
3
4
5

## Slide 152: HW Support for the OS
152
Mechanisms机制 to protect OS from processes
  Modes + virtual memory
Mechanisms to switch control flow between OS – processes
  System calls + exceptions
Mechanisms to protect processes from each other
  Virtual memory
Mechanisms to interact with I/O devices
  Primarily memory-mapped I/O

## Slide 153: Altering the Control Flow: System Calls
So far, we have branches and jumps
  They implement control flows within a program
Expected switch to the OS: system call instruction (syscall)
  A jump (or function call) to OS code
    E.g., in order to perform a disk access
    Also similar to a program-initiated exception
  Switches processor to kernel mode & disables interrupts
  Jump to a pre-defined place in the kernel
Returning from a syscall: use the eret instruction (privileged特殊的)
  Switch to user mode & enable interrupts
  Jump to program counter indicated by EPC
153

## Slide 154: Altering the Control Flow: Exception & Interrupts
154
Exceptions & interrupts implement unexpected switch to OS
  Exceptions: due to a problem in the program
    E.g., divide by zero, illegal instructions, page fault
  Interrupts: due to an external event
    I/O event, hitting clt+c, periodic timer interrupt
Exceptions & interrupts operate similar to system calls
  Set EPC & Cause registers
  Switch to kernel mode, turn off interrupts
  Jump to predefined part of the OS
  Return to user program using eret instruction

## Slide 155: Using Virtual Memory & Exceptions: Page Sharing
Example: Unix fork() system call
  Creates a 2nd process which is a clone of the current one
  How can we avoid copying all the address space
    Expensive in time and space
Idea: share pages in physical memory
  Each process gets a separate page table (separate virtual space)
  But both PTs point to the same physical pages
  Saves time and space on fork()
Same approach to support any type of sharing
  Two processes running same program
  Two processes that share data
155
creates a new process by duplicating the calling process

## Slide 156: Lecture 11.2 SIMD-Parallel Data

## Slide 157: Back to RISC-V: Vector Extensions (Draft)
To improve performance, SIMD instructions (and hardware)
  Fetch one instruction, do the work of multiple instructions
  OP denotes a vector instruction, prefix v – vector register
  vadd vd, vs1, vs2 (adds two vectors stored in vector registers)
  Assume vectors are 512-bits wide

## Slide 158: Summary
Flynn Taxonomy of Parallel Architectures
  SIMD: Single Instruction Multiple Data
  MIMD: Multiple Instruction Multiple Data
  SISD: Single Instruction Single Data
  MISD: Multiple Instruction Single Data (unused)
Intel AVX SIMD Instructions
  One instruction fetch that operates on multiple operands simultaneously
  512/256/128/64-bit AVX registers

## Slide 159: Lecture 12 Thread-Level Parallel Processing
159

## Slide 160: Machine Structures
Parallel Requests
  Assigned to computer
  e.g., Search “Cats”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates working in parallel at same time
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Main Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0

## Slide 161: Multiprocessor Execution Model
Each processor (core) executes its own instructions
Separate resources (not shared)
  Datapath (PC, registers, ALU)
  Highest level caches (e.g., 1st and 2nd)
Shared resources
  Memory (DRAM)
  Often 3rd level cache
    Often on same silicon chip
    But not a requirement
Nomenclature
  “Multiprocessor Microprocessor”
  Multicore processor
    E.g., four core CPU (central processing unit)
    Executes four different instruction streams simultaneously

## Slide 162: Multiprocessor Execution Model
Shared memory
  Each “core” has access to the entire memory in the processor
  Special hardware keeps caches consistent (next lecture!)
  Advantages:
    Simplifies communication in program via shared variables
  Drawbacks:
    Does not scale well:
      “Slow” memory shared by many “customers” (cores)
      May become bottleneck (Amdahl’s Law)
Two ways to use a multiprocessor:
  Job-level parallelism
    Processors work on unrelated problems
    No communication between programs
  Partition work of single task between several cores
    E.g., each performs part of large matrix multiplication

## Slide 163: Threads
Sequential flow of instructions that performs some task
  Up to now we just called this a “program”
Each thread has:
  Dedicated PC (program counter)
  Separate registers
  Accesses the shared memory
Each physical core provides one (or more)
  Hardware threads that actively execute instructions
  Each executes one “hardware thread”
Operating system multiplexes multiple
  Software threads onto the available hardware threads
  All threads except those mapped to hardware threads are waiting

## Slide 164: Operating System Threads
Give illusion of many “simultaneously” active threads
Multiplex software threads onto hardware threads:
  Switch out blocked threads (e.g., cache miss, user input, network access)
  Timer (e.g., switch active thread every 1 ms)
Remove a software thread from a hardware thread by
  Interrupting its execution
  Saving its registers and PC to memory
Start executing a different software thread by
  Loading its previously saved registers into a hardware thread’s registers
  Jumping to its saved PC

## Slide 165: Hardware Assisted Software Multithreading
Two copies of PC and Registers inside processor hardware
Looks identical to two processors to software (hardware thread 0, hardware thread 1)
Hyperthreading:
  Both threads can be active simultaneously
Memory
Input
Output
Bytes
I/O-Memory Interfaces
Processor (1 Core, 2 Threads)
Control
Datapath
PC 0
Registers 0
(ALU)
PC 1
Registers 1

## Slide 166: TLP
Thread Level Parallelism
  Thread: sequence of instructions, with own program counter and processor state (e.g., register file)
  Multicore:
    Physical CPU: One thread (at a time) per CPU, in software OS switches threads typically in response to I/O events like disk read/write
    Logical CPU: Fine-grain thread switching, in hardware, when thread blocks due to cache miss/memory access
    Hyperthreading (aka Simultaneous Multithreading--SMT): Exploit superscalar architecture to launch instructions from different threads at the same time!

## Slide 167: Parallel Programming Languages
Number of choices is indication of
  No universal solution
    Needs are very problem specific
  E.g.,
    Scientific computing/machine learning (matrix multiply)
    Webserver: handle many unrelated requests simultaneously
    Input / output: it’s all happening simultaneously!
Specialized languages for different tasks
  Some are easier to use (for some problems)
  None is particularly “easy” to use
COD
  Parallel language examples for high-performance computing
  OpenMP

## Slide 168: OpenMP Example
$ gcc-5 -fopenmp for.c;./a.out
% clang -Xpreprocessor -fopenmp -lomp -o for for.c; ./for
thread 0, i = 0
thread 1, i = 3
thread 2, i = 6
thread 3, i = 8
thread 0, i = 1
thread 1, i = 4
thread 2, i = 7
thread 3, i = 9
thread 0, i = 2
thread 1, i = 5
00 01 02 13 14 15 26 27 38 39
The call to find the maximum number of threads that are available to do work is omp_get_max_threads() (from omp.h).

## Slide 169: Synchronization
Problem:
  Limit access to shared resource to 1 actor at a time
  E.g. only 1 person permitted to edit a file at a time
    otherwise changes by several people get all mixed up
Solution:
Take turns:
  Only one person get’s the microphone & talks at a time
  Also good practice for classrooms, btw …

## Slide 170: Locks
Computers use locks to control access to shared resources
  Serves purpose of microphone in example
  Also referred to as “semaphore”
Usually implemented with a variable
  int lock;
    0 for unlocked
    1 for locked

## Slide 171: Review: Data Races and Synchronization
Two memory accesses form a data race if from different threads access same location, at least one is a write, and they occur one after another
If there is a data race, result of program varies depending on chance (which thread first?)
Avoid data races by synchronizing writing and reading to get deterministic behavior
Synchronization done by user-level routines that rely on hardware synchronization instructions

## Slide 172: RISC-V Atomic Memory Operations (AMOs)
AMOs atomically perform an operation on an operand in memory and set the destination register to the original memory value
R-Type Instruction Format: Add, And, Or, Swap, Xor, Max, Max Unsigned, Min, Min Unsigned
Load from address in rs1 to “t”
rd = ”t”, i.e., the value in memory
Store at address in rs1 the calculation “t” <operation> rs2
aq(acquire) and rl(release) to insure in order execution
amoadd.w rd,rs2,(rs1):
t = M[x[rs1]];
x[rd] = t; M[x[rs1]] = t + x[rs2]

## Slide 173: Deadlock
Deadlock: a system state in which no progress is possible
Dining Philosopher’s Problem:
  Think until the left fork is available; when it is, pick it up
  Think until the right fork is available; when it is, pick it up
  When both forks are held, eat for a fixed amount of time
  Then, put the right fork down
  Then, put the left fork down
  Repeat from the beginning
Solution?

## Slide 174: Shared Memory Multiprocessor (SMP)
Q1 – Single address space shared by all processors/cores
Q2 – Processors coordinate/communicate through shared variables in memory (via loads and stores)
  Use of shared data must be coordinated via synchronization primitives原型(locks) that allow access to data to only one processor at a time
All multicore computers today are SMP

## Slide 175: Shared Memory and Caches
What if?
  Processors 1 and 2 read Memory[1000] (value 20)
Processor
Processor
Processor
Cache
Cache
Cache
Interconnection Network
Memory
I/O
1000
20
1000
1000
1000
20
0
1
2

## Slide 176: Keeping Multiple Caches Coherent
Architect’s job: shared memory  keep cache values coherent
Idea: When any processor has cache miss or writes, notify other processors via interconnection network
  If only reading, many processors can have copies
  If a processor writes, invalidate any other copies
Write transactions from one processor, other caches “snoop” the common interconnect checking for tags they hold
  Invalidate any copies of same address modified in other cache

## Slide 177: Name of Common Cache Coherency Protocol: MOESI
Memory access to cache is either
  Modified (in cache)
  Owned (in cache)
  Exclusive (in cache)
  Shared (in cache)
  Invalid (not in cache)
Snooping/Snoopy Protocols
e.g., the Berkeley Ownership Protocol
See https://en.wikipedia.org/wiki/MOESI_protocol

## Slide 178: Remember The 3Cs?
Compulsory强制的(cold start or process migration, 1st reference):
  First access to block, impossible to avoid; small effect for long-running programs
  Solution: increase block size (increases miss penalty; very large blocks could increase miss rate)
Capacity (not compulsory and…)：
  Cache cannot contain all blocks accessed by the program even with perfect replacement policy in fully associative cache
  Solution: increase cache size (may increase access time)
Conflict (not compulsory or capacity and…):
  Multiple memory locations map to the same cache location
  Solution 1: increase cache size
  Solution 2: increase associativity (may increase access time)
  Solution 3: improve replacement policy, e.g.. LRU
Notes: (Capacity miss) That is the cache misses are due to the fact that the cache is simply not large enough to contain all the blocks that are accessed by the program.
The solution to reduce the Capacity miss rate is simple: increase the cache size.
Here is a summary of other types of cache miss we talked about.
First is the Compulsory misses. These are the misses that we cannot avoid. They are caused when we first start the program.
Then we talked about the conflict misses. They are the misses that caused by multiple memory locations being mapped to the same cache location.
There are two solutions to reduce conflict misses. The first one is, once again, increase the cache size. The second one is to increase the associativity.
For example, say using a 2-way set associative cache instead of directed mapped cache.
But keep in mind that cache miss rate is only one part of the equation. You also have to worry about cache access time and miss penalty. Do NOT optimize miss rate alone.
Finally, there is another source of cache miss we will not cover today. Those are referred to as invalidation misses caused by another process, such as IO , update the main memory so you have to flush the cache to avoid inconsistency between memory and cache.

## Slide 179: Acknowledgements
These slides contain material from courses:
  UCB CS152.
  UCB CS61C.
  Stanford EE108B